## Slide 1: Experiment No. 04 and 05 Design and Implementation of Finite Impulse Response (FIR) Filter and adaptive filter(LMS)

## Slide 2: Question-1 Plot Hamming, Hann and Kaiser window functions used in design of a FIR filter. Comment on the results Solution
beta=5.2;
N=20;
n=1:1:20;
y=hamming(N);
y1=hann(N);
y2=kaiser(N,beta);
plot(n,y,'k^-',n,y1,'kd:',n,y2,'k*:’)
xlabel('n')
ylabel('h(n)')
legend('Hamming','Hann','Kaiser’)
grid on

## Slide 3: Let us observe the impact of window function in impulse response of a LP FIR filter.
Compare between ideal and practical FIR LP filter .
Question-2

## Slide 4: Solution
N=25; %Range of sample
n=-N:1:N;
fc=0.1930; %cutoff frequency of LP filter
hd=sinc(2*fc*n);%impulse response of ideal LP filter
subplot(2,1,1)
stem(n,hd)
xlabel('n')
ylabel('hD')
title('Impulse Response of Ideal LP FIR Filter')
grid on
wn=hann(2*N+1);%hanning Window
subplot(2,1,2)
h=hd'.*wn;%Practical Impulse Response
stem(n,h)
xlabel('n')
ylabel('h')
title('Impulse Response of Practical LP FIR Filter')
grid on

## Slide 5: Homework
Compare the performance of ideal and practical LP filter using hamming window function for the following specifications.
Fs = 8KHz
Passband edge frequency 1.5 KHz
Transition width 0.5KHs
Stop band attenuation >50dB

## Slide 6: Question no 3
Apply LMS adaptive filter for a speech signal. Verify the sound quality using: sound(s), sound(sn) and sound(e) taking 20,000 samples in above code.

## Slide 7: solution
clear all
close all
load handel %original signal
s = y(1:4000); %taking 4000 samples of sound wave
s=s';
noise = 0.12*randn(1,length(s)); % random noise
sn=s+noise;% noisy signal
%LMS Algorithm
lmsfilt = dsp.LMSFilter('Length', 16, 'Method', 'Normalized LMS', 'StepSize', 0.02); [y,e,w] = lmsfilt(noise', sn'); %filtering the signal with LMS of step size mu = 0.02
t=1:1:length(s);
t=t/500;
subplot(3,1,1)
plot(t,s,'r')
title('Original Signal')
subplot(3,1,2)
plot(t,sn,'b')
title('Noisy Signal')
subplot(3,1,3)
plot(t,e,'k')
title('De-noised Signal')